## Slide 1: MICRO-CONTROLLER AND EMBEDDED SYSTEMS (MES)

## Slide 2
Businesses runs on software and softwares run on hardware

## Slide 3
Operating system is a bridge that connects software and hardware

## Slide 4
Hardware of a computer essentially comes in 2 forms: microprocessors and microcontrollers

## Slide 5
Differences between microprocessors and microcontrollers
Parameter | Microprocessor | Microcontroller
Definition | IC that has only CPU inside it and RAM, ROM and other peripherals need to be added externally | IC that has integration of CPU RAM, ROM and other peripherals
Tasks used | General purpose | Specific purpose
Preference | Relationship between input and output is not clearly defined | Relationship between input and output is clearly defined

## Slide 6
Parameter | Microprocessor | Microcontroller
Suitability for embedded applications | Not suitable | Ideally suitable due to low power consumptions
Suitability for general purpose applications | Ideally suitable due to capability of satisfying huge resource demands | Not suitable
Price | Costlier | Cheaper
Speed | High (1Ghz) | Slow (20-50Mhz)
Memory | External (in GBs) | KBs of internal for RAM and ROM

## Slide 8
ARM stands for Advanced RISC Machine. It is one of the most licensed and extensive processor cores in the world.
Specially used in portable devices like digital cameras, mobile phones, home network modules, wireless communication technologies, etc..
Advanced RISC Machine Architecture is better than x86.
ARM Processor is not only limited to mobile phones but is also used in Fugaku, the world’s fastest supercomputer.
ARM can be used as a microprocessor, microcontroller and both
ARM FeatuRes

## Slide 9
MODULE-1
ARM processor fundamentals
MODULE-2
ARM Instruction Set
C compilers with ARM
MODULE-3
ARM C programming with optimization
ARM ALP programming
About Microcontrollers and Embedded systems

## Slide 10
MODULE-4
Sensors and actuators
MODULE-5
Real time Operating Systems (RTOS)
Embedded System Development Environment
Embedded System components

## Slide 13
Arduino is a open-source project.
Supports hardware and software platform to design and build electronic devices.
The designs of Arduino boards use a variety of controllers and microprocessors.

## Slide 14
Raspberry Pi, developed by Raspberry Pi Foundation in association with Broadcom, is a series of small single-board computers and perhaps the most inspiring computer available today.
It is a cheap, credit-card-sized device that uses a daily keyboard and mouse and joins to a TV or computer monitor.
It is a thin weighable computer that let every person to explore the internet and watching high-definition video, word-processing, to creating spreadsheets, and it can do every possible thing we'd expect a desktop computer to do and playing sports.

## Slide 16
NVIDIA Jetson Nano is an embedded system-on-module
128 core MAXWELL GPU
ARM CPU
Useful for deploying computer vision and deep learning

## Slide 17
RISC – Reduced Instruction Set Computer
CISC – Complex Instruction Set Computer

## Slide 18
RISC – Simple but powerful
CISC – Complex
Hardware

## Slide 19
RISC – Single cycle per instruction
CISC – One or Two cycles per instruction

## Slide 20
RISC – relies on intelligence of software and lesser complex hardware
CISC – relies on complex hardware

## Slide 21
Compiler
Code Generation
Processor
Greater Complexity
Compiler
Code Generation
Processor
Greater Complexity
RISC – compiler complexity
CISC- hardware complexity
CISC
RISC

## Slide 22
Major design rules of RISC
Instructions
Simple
Synthesis
Fixed length
Prefetch
Reduced number of instructions
One clock cycle
Derive new instructions from old
CISC drawbacks: variable size instructions, many clock cycles might be required

## Slide 23
Pipelines: Instructions divided into smaller units and run parallelly in pipelines
Instructions decoded in one pipeline stage
CISC drawbacks: microcode required

## Slide 24
RISC has too many general purpose registers
CISC has few dedicated registers
Register
Data or Address

## Slide 25
Operating directly on memory not allowed in RISC unlike CISC
Register
Memory
LOAD
Register
Memory
STORE

## Slide 26
ARM

## Slide 27
Extended battery operation
High code density
-due to cost
-physical size restrictions
Price sensitive
Smaller area used by embedded processor
Incorporated hardware debug technology

## Slide 29
Instruction set,
Special registers,
Special instructions

## Slide 30
Instruction SET FOR EMBEDDED SYSTEMS
Few instructions incur variable cycle. Load and Store depends on number of registers used

## Slide 31
Inline barrel shifter leading to complex instructions
Thumb 16 bit instruction set
Conditional execution
Enhanced Digital Signal Processing Instructions

## Slide 33
Embedded SYSTEMS
An embedded system is a combination of computer hardware and software designed for a specific function.
Embedded systems may also function within a larger system.
The systems can be programmable or have a fixed functionality.

## Slide 34
Embedded SYSTEMS HARDWARE BASED on ARM
ARM Processor
Interrupt Controllers
AHB Arbiter
Memory Controller
AHB External bridge
SRAM, FLASH, DRAM
AHP-APB Bridge
Real time clock
Serial UART
Ethernet
Counters/Timers
Driver

## Slide 35
ARM BUS TECHNOLOGY
PCI Bus:
Used in x86
Interconnect Hard disk drives and video cards
External or off-chip

## Slide 36
ARM Bus:
Used in Embedded devices
Interconnect different peripherals with ARM Core
Internal or on-chip

## Slide 37
ARM BUS – MASTER SLAVE ARCHITECTURE
Master- ARM Core processor who can initiate data transfer
Slaves – Peripherals – capable of responding to transfer requests

## Slide 38
ARM BUS – ARCHITECTURE LEVELS
Electrical characteristics and bus width
Protocol between processor and peripherals

## Slide 40
ASB – ARM System Bus
AHB – ARM High Performance Bus with larger bandwidths (64 /128 bit)
Multi-layer AHB and AHB Lite
APB – ARM Peripheral Bus with slower bandwidth
AHB New interconnects supports multiple processors, supporting operations in parallel

## Slide 41
MEMORY
Embedded system needs memory to store and execute code

## Slide 42
Storage Tradeoffs

## Slide 44
TYPES OF MEMORY
Read Only Memory
Permanently set during production time and cannot be reprogrammed
Contains boot code

## Slide 45
Can be written but slow
Not for dynamic data
Suitable for firmware data
Erasing and writing of flash is software controlled

## Slide 46
DRAM cheaper than SRAM
DRAM slower as it requires refresh than SRAM

## Slide 47
Can run at much higher clock speeds than conventional memory
It synchronizes itself with the computer’s system clock. This makes it easy to manage faster

## Slide 48
Peripheral device
Connect ARM to outside world
Comprises of input and output devices
Can be on-chip
Can connect other sensors and actuators
ARM peripherals are memory-mapped. (memory address registers).
Controllers are specialized peripherals to control access to memory or interrupts

## Slide 49
Memory Controllers
Connect different types of memory to AHB
On power up, certain memory devices are made active.
These memory devices execute initialization code.
They also enable refreshing required as in DRAM.

## Slide 50
Interrupts are raised to gain attention
In this case, interrupts raised by peripherals to get attention of ARM processor.
Interrupts go through Interrupt controllers

## Slide 51
Peripherals
Standard Interrupt Controller (SIC)
IGNORE OR ALLOW
ARM
Interrupt Handler

## Slide 52
Peripherals
Vector Interrupt Controller (VIC)
ARM
Interrupt Handler

## Slide 53
Embedded SYSTEMS SOFTWARE
HARDWARE DEVICE
DEVICE DRIVER
INITIALIZATION CODE
OPERATING SYSTEM
APPLICATIONS

## Slide 54
An embedded system gets into action by first executing boot code (initialization code)
It sets up memory devices, caches, peripheral devices
Deals with administrative work before actual OS image is loaded

## Slide 55
Phase-1: Initialize hardware configuration be reorganizing memory

## Slide 56
Phase-2: Diagnostics
Diagnose whether hardware is working or not
Helps in isolating faults

## Slide 57
Phase-3: Booting an image
Load relevant OS image
Copy code and/or data into RAM
Sometimes image decompression is required
Complex when task is to boot from multiple OS images

## Slide 58
Operating Systems
OS is like manager which manages various resources like memory, processor and peripherals
ARM has more than 50 OS, but 2 categories: RTOS and PSOS

## Slide 59
It has deadlines and guaranteed response
Hard RTOS provides guaranteed response
Soft RTOS provides good response
RTOS do not have secondary storage
RTOS

## Slide 60
POS
Platform Specific Operating Systems
No deadlines
Large exclusive memory manager for real time applications
Tend do have secondary storage

## Slide 61
Embedded SYSTEMS APPLICATIONS

## Slide 62
ARM processors suitable to applications that are price sensitive and high volume.
ARM processors not found in applications that require leading edge high performance.

## Slide 63
ARM CORE PROCESSOR COMPONENTS
View of programmer
Data flow through various functional units is shown
Bus communication is also depicted
Von-nuemann vs Harvard architecture

## Slide 64
Data/Instruction
Instruction Decoder
Sign Extend
Register file r0- r15
ALU
Rn
Barrel Shifter
Rm
N
MAC
Acc
Result
Rd
Address Register
Incrementer
pc
Address
Write
Read
A
B
r15

## Slide 66
ARM Register
Data or Address
Prefixed with letter r
18 active registers in user mode:
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13-sp
r14-lr
r15-pc
sp- Stack pointer
lr-Link register
pc-Program Counter
Registers r0 to r13 are orthogonal
cpsr
spsr
cpsr- Current Program status register
spsr-Saved program status register

## Slide 67
Program STATUS REGISTER
Mode
T
F
I
V
C
Z
N
0
4
5
6
7
28
29
30
31
Processor Mode
Thumb state
Interrupt Masks
Condition flags
Flags
Status
Extension
Control

## Slide 68
PROCESSOR MODES
PRIVILEGED
NON-PRIVILEGED
In privileged mode- full read-write access to cpsr
In non-privileged mode – read only access

## Slide 69
PROCESSOR MODES
Processor Mode | Explanation | Type
Abort | Failure to access memory | Privileged
Fast Interrupt Request | Peripherals signaling attention of processor with high priority | Privileged
Interrupt Request | Peripherals signaling attention of processor with normal priority | Privileged

## Slide 70
Processor Mode | Explanation | Type
Supervisor | OS mode | Privileged
System | Special version of user mode that allows full readwrite access to the user | Privileged
undefined | Wrong instruction | Privileged
User | Enter user mode | Non-Privileged

## Slide 71
bANKED REGISTERS
Visible 17 registers
Hidden 20 registers called Banked Registers

## Slide 72
Changing mode on exception
Interrupts and exceptions changes mode
Reset, interrupt request, fast interrupt request, software interrupt, data abort, prefetch abort, undefined instruction

## Slide 73
Every processor mode except user mode can change mode by directly writing to cpsr
Can be changed by program or hardware
Saved program status register stores previous modes cpsr
spsr only modified with privileged mode
spsr only done when hardware changes processor mode

## Slide 74
PROCESSOR MODE VALUES

## Slide 75
ARM INSTRUCTION SETS
ARM
THUMB
JAZELLE
In state field T=1 => Thumb Mode,
J=1 => Jazelle Mode

## Slide 76
ARM vs THUMB
THUMB
ARM
Parameter
16 bit
32 bit
Instruction size
30
58
Core
instructions
Only branch
most
Conditional
Execution
Separate access
to barrel shifter
and ALU
Combined access
to barrel shifter
and ALU
Data processing
No direct access
Read
-
write in
privileged access
Program status
register
8GP +7high+pc
15 GP + pc
Register usage

## Slide 78
Interrupt Mask
Interrupt Service
IRQ- Interrupt Request
FIQ- Fast Interrupt Request

## Slide 79
CONDITION FLAGS
Mainly affected by ALU operations
When
Flag Name
Flag
DSP instruction
overflow
Saturation
Q
Signed overflow
oVerflow
V
Unsigned carry
Carry
C
Comparison results
in equality
Zero
Z
Bit 31 is 1
Negative
N

## Slide 80
Conditional execution will determine whether ARM processor will execute a specific instruction or not

## Slide 82
Pipelines: Instructions divided into smaller units and run parallelly in pipelines
Instructions decoded in one pipeline stage

## Slide 83
ARM 3 StAGE PIPELINE
Fetch an instruction from memory
Decode identifies instruction
Execute executes the instruction and writes result back to register

## Slide 84
EXAMPLE PIPELINE SEQUENCE
Filling of Pipelines

## Slide 85
5 stage pipeline
7 stage pipeline
Increased pipeline length a tradeoff between performance and latency

## Slide 86
PIPELINE EXECUTING CHARACTERISTICS
Pipelines and Interrupts

## Slide 87
Pipelines and Program Counter

## Slide 88
Execution of branch instruction causes ARM core to flush its pipeline
Loading the new branch address prior to the execution of instruction.
Instruction in the execute stage will complete even though an interrupt has been raised.

## Slide 89
Exceptions
Interrupts
When exception or interrupt, processor sets pc to special address from vector table.

## Slide 91
ARM processor is given extensions to improve performance, do extra functionality and provide flexibility.

## Slide 92
ARM EXTENSIONS
CACHE and TIGHTLY COUPLED MEMORY
MEMORY MANAGEMENT
COPROCESSOR

## Slide 93
ARM Core
Logic and Control
Unified cache
AMBA bus interface unit
Main Memory
On-chip AMBA Bus
Von Neuman

## Slide 94
ARM Core
Logic and Control
AMBA bus interface unit
Main Memory
On-chip AMBA Bus
Data cache
Instruction cache
D
D
I
I
D + I
Harvard

## Slide 95
ARM Core
Logic and Control
AMBA bus interface unit
Main Memory
On-chip AMBA Bus
Data cache
Instruction cache
D
D
I
I
D + I
Harvard with TCM
Data TCM
Instruction TCM
D
D
I
I

## Slide 96
Nonprotected memory
Memory Protection Units (MPU) with limited protection.
Memory Management Units (MMU) with full protection
ARM CORE MEMORY MANAGEMENT HARDWARES

## Slide 97
COPROCESSORS –ADDITIONAL TO PROCESSORS

## Slide 98
Coprocessors extend the basic capabilities of processors